LAN
A computer network that spans a relatively small area. Most often, a LAN is confined to a single room, building or group of buildings

---
Features Of LAN
- The sharing of resources
- Data transfer and e-mail
- Improve the reliability
- Easy to distributed processing

---
Components of LANs
- Network Adapter
- Network Medium
- Cable Connectors
- Power Supply
- Hub/Switch/Router
- Network Software

---
LAN Standards
- Network standards define guideline that specify the way computers access the medium to which they are attached.
- The guideline also describe the type of medium used, the speeds used on different type of physical cable or wireless technology used
- The well known standards adopted by the IEEE are 802 standards.

---
IEEE802 standards
- 802.3
- 802.7
- 802.8
- 802.11

---
802.3 Ethernet LAN
- It is the standard for an Ethernet LAN.
- In 802.3, Ethernet refers to the physical cabling, while the way data is transmitted through the cable is called Carrier Sense Multiple Access/Collision Detection(CSMA/CD)
- This method of transmission requires that only one device in network can transmit at a time. If another device can sense that a transmission is already in the cable, it will have to wait

---
802.7 Broadband LAN
- It is a Standard Specification for Broadband LAN
- This 802.7 standard provides specifications for the design,installation and testing needed for broadband transmission
- Broadband transmission allow simultaneous multiple transmission or signal using different communication channels at the same time

---
802.8 Fibre-Optic LAN and MAN
- Specification for Fibre-Optic LAN and MAN are given under the 802.8 standard.
- This standard gives the recommendation for the configuration and testing of fibre-optic Local Area Network and Metropolitan Area Networks

---
802.11 Wireless LAN
- This standard defines communication between a wireless computer or client and an access point or between two wireless computers or clients.
- The 802.11 standard uses the 2.4GHz frequency band to transmit data up to 2Mbps.

---
Channel Access Method
- Channel access method (CAM) is used to allow network terminals to share media capacity through a multipoint transmission medium. CAM examples include bus, hub, wireless and ring networks.
- A channel access scheme is based on a multiplexing method, which allows several data streams or signals to share the same communication channel or physical medium.
- It is also based on a multiple access protocol and control mechanism known as media access control (MAC).

---
Channel Access Method protocol features
- Physical layer multiplexing
- The media access control layer, which handles addressing and collision prevention
- Token passing
- Polling, a continuous slave/master data querying process
- Contention or node network access competition

---
Channel Access Method Schemes
- Frequency division multiple access
- Time division multiple access
- Code division multiple access
- Spatial division multiple access

---
ALOHA
ALOHA is a system for coordinating and arbitrating access to a shared communication Networks channel.

---
Pure Aloha

---
Slotted Aloha

---
Carrier Sense Multiple Access
- Carrier Sense Multiple Access (CSMA) is a network protocol that listens to or senses network signals on the carrier/medium before transmitting any data.
- CSMA works on the principle that only one device can transmit signals on the network, otherwise a collision will occur resulting in the loss of data packets or frames.

---
CSMA access modes
- 1-persistent
- Non-persistent
- P-persistent
- O-persistent

---
CSMA with collision detection
- A set of rules determining how network devices respond when two devices attempt to use a data channel simultaneously.
- Standard Ethernet networks use CSMA/CD to physically monitor the traffic on the line at participating stations. If no transmission is taking place at the time, the particular station can transmit.
- If two stations attempt to transmit simultaneously, this causes a collision, which is detected by all participating stations.
- After a random time interval, the stations that collided attempt to transmit again.

---
CSMA with Collision Avoidance
- In contrast to the Carrier Sense Multiple Access/Collision Detect (CSMA/CD) protocol, which handles transmissions only after a collision has taken place, CSMA/CA works to avoid collisions prior to their occurrence.
- CSMA/CA increases network traffic as it requires sending out a signal to the network even before transmitting any real data. This is to listen for any collision scenarios in the network and to inform other devices not to transmit.
- A node listen to the broadcast channel for a pre-specified time frame to determine if another node is broadcasting on the channel inside the wireless range.